## Slide 1
Berry Collection System
How the Artix-7 game tracks, draws, collects, scores, celebrates, and resets strawberries.
5 persistent berries · 1-cycle score pulse

## Slide 2
The berry system is a tiny state machine
VGA rendering asks “what tile is here?” while gameplay asks “did the player touch a live berry?”
Tile map
`tile_at_tile()` marks live berry tiles as `STRAWBERRY`.
→
draws
Sprite ROM
VGA samples the strawberry frame and outputs 12-bit RGB.
→
touches
Berry FSM
A touched berry clears one bit and emits `collect_berry`.
→
scores
Score
One pulse increments the SSD counter by exactly one.

## Slide 3
Each strawberry is a 2×2 tile footprint
The coordinate is the top-left tile; the mask covers four tiles so the visual and collectible area match.
A berry at (2, 1) occupies (2..3, 1..2)
localparam BERRY_COUNT = 5;
BERRY0_X, BERRY0_Y // top-left tile
tx >= BERRY_X && tx <= BERRY_X + 1
The `berries_present` register controls which of those 2×2 footprints still exists.

## Slide 4
`berries_present` is the source of truth
Five bits represent five strawberries. Reset or spike restores all bits; collection clears just the touched berry.
Before collection
berries_present = 5'b11111
All five strawberries draw and can be collected.
After touching berry 2
touched_berries = 5'b00100
berries_present <= berries_present & ~touched_berries
Only berry 2 disappears; the other bits stay live.

## Slide 5
Collection checks both current and next corners
That avoids missing berries during dashes and keeps visual contact aligned with gameplay contact.
current corners + next corners
berry_mask(player_left, player_top)
berry_mask(player_right, player_bottom)
berry_mask(left, top) | berry_mask(right, bottom)
All masks OR together into `touched_berries`.

## Slide 6
The FSM turns overlap into one score pulse
Without the pulse, the score would climb every clock while the player overlaps the berry.
BERRIES_READY
Wait until `(berries_present & touched_berries)` is nonzero.
→
overlap
BERRIES_UPDATE
Clear touched bits and set `collect_pulse` for one clock.
→
next
BERRIES_READY
Return to waiting. The score saw exactly one pulse.

## Slide 7
Rendering and win behavior stay separate from collection
The visible sprite is a presentation of state; the FSM owns game truth.
Draw priority
celebration → Madeline → strawberry → spike → solid tile → background
Sprite scaling
The strawberry ROM is 16×16; VGA maps it across a 32×32, 2×2-tile area.
Score
`collect_berry` increments the SSD counter. Reset or spike clears it.
Win reset
`all_berries_collected` starts a 10-second timer, shows celebration, then resets the game.